## Slide 1: Maker’s course Flash Memory, File System and WebServer
Gil Tal.
Dec 2024

## Slide 3: Agenda:
Flash memory
EEPROM and usage on our platform
Flash memory partition options
SPIFFS – SPI flash file system
SD card file system (FAT32)
WebServer

## Slide 4: Flash memory
sector, programable memory
Most common interface is SPI (1,4 or 8 bits)
Sector based (4KB, 8KB, 16KB, 64KB, 128KB) – ESP32’s flash sector size is 4KB
We can only erase full sectors
After erasing a sector, all of the sector’s bits are set at logic 1(0xFFFFFFFF)
We can set any bit to 0, but cannot set it back to 1 unless we erase a complete sector
Sector can be erased around 100000 times!! That’s all!!
Erase operation is long (~10ms)
Not suitable serving a memory for counters (will stop functioning after 100000 time!)
Sectors can be protected

## Slide 5: EEprom memory
Small sizes (2KB to 64KB)
Size to price ratio is bad 
You can write to any byte any data
Most common interface is I2C
Very slow and mostly used for saving configuration data
ESP32’s EEPROM is emulated on the main flash and is occupying one sector (4KB)
How to use:
  EEPROM.begin(512); // Size up to 4096
  EEPROM.write(12/*Address*/,100/*Data*/);
  EEPROM.commit(); // Save the data

## Slide 6: ESP32 Flash memory Partitions
Application partition 1
Application partition 2
SPIFFS
1.2MB
1.2MB
1.5MB
Partition table is flexible
Can be set through visual micro

## Slide 7: SPIFFS – SPI flash system
Resides on the ESP32’s flash memory
How to use:
  Create a data folder in the sketch folder
  Upload it through visual micro
  Files accessible in our code
Look @ ESP32_SPIFFSdemo.ino
  Copy the data folder into sketch folder

## Slide 8: File System - SPIFFS
void setup() { // Launch SPIFFS file system
if (!SPIFFS.begin())
{
Serial.println("An Error has occurred while mounting SPIFFS");
}
}
void loop() {
File file = SPIFFS.open("/TestFile.txt");
char buf[100];
int fileSize;
if (!file)
{
Serial.println("Failed to open file for reading");
while (1);
}
Serial.print("File size: ");
Serial.println(fileSize = file.size());
if (fileSize < 100)
{
file.readBytes(buf, fileSize);
for (size_t i = 0; i < fileSize; i++)
{
printf("%c", buf[i]);
}
printf("\n");
}
file.close();
while (1);}

## Slide 9: File System – SD card over SPI
FAT32 full support
Possible to load new code from SD!
#include "FS.h"
#include "SD.h"
SPIClass SDspi(FSPI);
bool SDmountOK;
PCF8574 pcf8574(0x21);
// the setup function runs once when you press reset or power the board
void setup() {
Serial.begin(115200);
pcf8574.begin();
pcf8574.pinMode(P0, OUTPUT); // SD CS
pcf8574.digitalWrite(P0, LOW); // Set SD card chip select to low (enabled)
SDspi.begin(15, 36, 13, -1);
if (!SD.begin(50, SDspi, 1000000, "/sd", 5))
{
printf("Failed to mount SD card!\n");
SDmountOK = false;
}
else
{
printf("SD card mounted on VSPI.\n");
SDmountOK = true;
}
}// the loop function runs over and over again until power down or reset
void loop() { if (SDmountOK)
{
listSDcardFiles("/");
}
while (1);}

## Slide 10: Wi-fi basics
Wi-Fi basics:
  Family of wireless networking technologies
  IEEE 802.11 family of standards
  Used for local area networking of devices and Internet access
  20-150 meters range
  Standard defines 16 channels for communication
    Enables multiple access points at the same physical location

## Slide 11: Communication options
AP – Access point
STA – Station
An end point device
Enable the creation of a local Wi-Fi network
We connect to access point
With or without access to the internet
Uses a specific channel which can be modified while operating
Has limitation for number of connected devices
Has a name and an optional password
Can use an encrypted communication protocol
Connects to an AP
While searching for an AP needs to scan different channels until found
Station name and password can be saved on EEPROM, SPIFFS or SDCARD
AP
End Point device

## Slide 12: Wi-fi basics: our esp32
Runs full network stack
Can function as:
  AP
    By default, enables up to 4 users
  STA
  Both*

## Slide 13: HTML
Hyper Text Markup Language
Is the standard markup language for documents designed to be displayed in a web browser
It can be assisted by technologies such as Cascading Style Sheets (CSS) and scripting languages such as JavaScript
https://www.w3schools.com/ - great site for learning and designing web pages

## Slide 14: webserver
Web pages are hosted on a webserver
  Most commonly written in HTML5 + JAVA script
  There are various HTML5 emulators out there
Has a specific IP address (192.168.14.1 for example)
Is a passive device
We need a browser to access it
  Browser is executing the HTML5 code
  The communication protocol is HTTP
There are large number of hosting providers
IP address can be replaced by a name
  DNS server translates the name to the specific IP address
ESP32 can run a webserver! 

## Slide 15: Webserver – what can we do with it?
Have
a nice GUI to communicate with the ESP32 using a browser
Control
IOs
Get
information from our ESP32
Such as temperature, humidity depending on what we connected
Send
data to the ESP32
Files
Raw data

## Slide 16: Webserver – workflow
We need to initialize:
WiFi
Webserver
Prepare the HTML for the pages
Handle the client which interacts with the browser
Process the incoming data from the browser to perform actions on the ESP

## Slide 17: Webserver – html data
For static data with pre-defined start conditions:
const char mainMenuPage[]PROGMEM = R"rawliteral(
  HTML Data
)rawliteral";
For dynamic data with interactive page we need to use String and build the page in real time, Or use a call back function with: %VALUE% in our HTML code (refer to the code example)

## Slide 18: How does it look like…

## Slide 19: Generating Icons for my web page
https://www.base64-image.de/
How to use:
Prepare an image of size 100x100 of type PNG:
.configButton {background-color: rgb(255,255,255); border-radius: 50px;width: 50px; height: 50px;
background-image: url('data:image/png;base64,iVBORw…….');
background-position: center;
background-repeat: no-repeat;
background-size: 80px 80px;
}

## Slide 20: Multicast DNS
Domain Name System
MDNS – Is a zero-configuration service
Enables usage of names instead of IP address
Our ESP32 runs Multicast DNS (MDNS)
Windows and Apple devices can work with MDNS
Sadly Android does not 
Usage:
  esp32.local
  No MDNS support - 192.168.4.1 (just an example IP)